## Slide 1: Course
Take a long time
Cost a lot
Neural networks contain a lot of information. Numerous parameters make networks very big.
NVDLA is a kind of accelerator. When simulate it on computer, it will be run on virtual platform which will take many resources. The system(linux kernel) is also one reason make the process very slow.

## Slide 3: Introduction to this technology
NVDLA
Our method

## Slide 4: NVDLA core block diagram
yolo v3

## Slide 5
Source:
https://blog.csdn.net/leviopku/article/details/82660381
CONV. BN. ReLU. ResNet. Up-sampling. Concatenation

## Slide 7: Our method
Interface
CDMA
CSC
CMAC
Adder
Truncation
Set all hardware parameters configurable to get the optimal configuration information fastly.

## Slide 8
SRAM size: From 6MB to 4MB
YOLOV3 RESULT TABLE (int8) |  |  |  |  | 
CASES | CMAC CELLS | SRAM SIZE (MB) | NVDLA Inference Time and Data Transfer Time (Milliseconds) | Up-samling Time (CPU) (Milliseconds) | Total Inference Time (Milliseconds)
1 | 8 | 6 | 9.67 | 5.07 | 14.74
2 | 16 | 6 | 8.79 | 2.18 | 10.97
3 | 32 | 6 | 8.07 | 2.11 | 10.18
4 | 16 | 4 | 51.16 | 2.18 | 53.34
In case 4:
The data transfer process elongated, which makes the computing units wait for the data transferring.

## Slide 9
SRAM size: From 4MB to 2MB
FASTER RCNN RESULT TABLE |  |  | 
CASES | CMAC CELLS | SRAM SIZE (MB) | TOTAL Inference Time (Milliseconds)
1 | 8 | 4 | 19.41
2 | 16 | 4 | 18.12
3 | 8 | 2 | 60.24

## Slide 10: Verification: yolo v3
The time consumed by different layers is added together to get the total inference time: 0.0515s
total_time = 0.0012056780555555556 +0.009336928703703697 + 0.006109037037037037 + 0.006215587351851845 + ......
Totally 75 values

## Slide 11: Verification: First layer
Time: 0.0012056780555555556s
Size : 0.495941162109375 MB
  4153344(input feature map) + 6912(weights)
DRAM -> SRAM: 0.00001583933 s
SRAM -> CBUF: 17 chunks
One CBUF chunk:

## Slide 12: Verification: an example
Fully connected layer:
Input_feature_map: 8*8*32
Kernel_size: 8*8*32 kernel_number: 16
Precision: int16 Total_input_bits: 557056
DRAM->SRAM
SRAM->CBUF
CBUF->ABUF
ABUF->DBUF
0
1.584e-5
seconds
2.356e-7
2.481e-7
DBUF->SDP->SRAM
6.296e-9
1.481e-9
1.608e-5
1.633e-5
1.633e-5
1.633e-5
1.584e-5
557056
557056
768
512